## Slide 1
🎸 AXEL ROSE
WeGo
Bus Performance Analysis
350,329 stop observations. One big question:
why is everyone running early?
🚌💨

## Slide 2
📊 The Big Picture
64.4%
of stops are served EARLY
(more than 1 min ahead of schedule)
Mean adherence: −3.1 min
34.0%
On-time
64.4%
Early
1.6%
Late
350K
+
Total stops
💡 Early = missed buses too. It's not just about being late.

## Slide 3
🗺️ Where Does It Go Wrong?
🧭
Direction
Both inbound & outbound run early — no direction is immune. The fleet-wide mean is −3.1 min across all directions.
🛣️
Route
Top 20 routes by volume show wide variation. Some routes average −6 min early. Scheduling, not traffic, is the culprit.
📍
Location
Stop-level map reveals spatial clusters of early-running — terminus stops and low-traffic corridors are the worst offenders.

## Slide 4
⏰ Timing is Everything
Chart: Adherence by hour of day
| 12a | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12p | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11
Mean adherence (min) | -2.1 | -1.8 | -1.5 | -1.2 | -1 | -1.8 | -2.5 | -3.2 | -3 | -2.9 | -3.1 | -3.3 | -3.2 | -3.4 | -3.5 | -3.6 | -3.2 | -2.8 | -3 | -3.3 | -3.5 | -2.9 | -2.4 | -2
Chart: By day of week
| Mon | Tue | Wed | Thu | Fri | Sat | Sun
Mean adherence (min) | -3.2 | -3.1 | -3.3 | -3.2 | -3 | -2.7 | -2.4
🔑 Early-running is worst in afternoon off-peak hours. Weekends are slightly better — less pressure to run ahead.

## Slide 5
🚌 Does the Driver Matter?
12.7%
of adherence variance
explained by operator
299 operators analysed
(≥50 obs each)
IQR of operator means
−4.2 to −1.9 min
Best operator average
−10.5 min early
Worst operator average
+1.3 min (barely late!)
Std dev across operators
1.98 min
🎯 Drivers matter — but the schedule is doing most of the damage. Fix scheduling first, then coach the outliers.

## Slide 6
🚌🚌 Bunching & Gapping
When buses run early, they bunch together — leaving huge gaps behind them
Chart: Headway status breakdown
| Bunching (<50%) | Acceptable (50–150%) | Gapping (>150%)
% of stops | 6.7 | 85 | 8.2
Pearson r = −0.308
Spearman ρ = −0.500
📉 Earlier buses = shorter headway = bunching
📈 Later buses = longer headway = gaps for riders
🔄 Spearman (0.50) >> Pearson (0.31) → nonlinear effect at the extremes
🚶 Riders don't just miss early buses — they wait twice as long after
💥 85% of stops are within acceptable headway — but the compounding effect of early-running creates real passenger pain.

## Slide 7
So... What Do We Do?
01
Fix the schedule
Mean adherence of −3.1 min fleet-wide means the schedule is systematically too loose. Tighten run times, especially in off-peak.
02
Target early-running routes
A handful of routes skew heavily early. Route-specific timing point adjustments could dramatically improve overall OTP.
03
Coach the outliers
12.7% of variance is operator-driven. The worst operators run 10+ min early — targeted coaching could close that gap.
04
Monitor headway, not just adherence
A bus can be "early" but still provide good service. Headway deviation tells the real passenger experience story.

## Slide 8
Thanks for riding
with Axel Rose 🎸
Any questions? (We promise we ran on time.) 🚌
WeGo Bus Performance Analysis • 350,329 observations • Spring 2026